## Slide 1: Toward Consistent, Usable Security Risk Assessment of Medical Devices
Penny Chase and Steve Christey Coley
The MITRE Corporation
June 3, 2016
Approved for Public Release; Distribution Unlimited 16-1984

## Slide 2: (In)security of Medical Devices
Medical devices increasingly rely upon computers, software, and networking
Medical devices often incorporate third-party software, such as operating systems for controller workstations, real time operating systems, databases, middleware, remote access
Medical devices are subject to regulation, which can impact the ability to patch and reconfigure, leaving devices running old, vulnerable software
Clinical trials are small, so many flaws aren’t discovered until device is on the market
Few manufacturers incorporate security testing

## Slide 3: FDA and Device Security
Vision: To foster a community-driven collaborative environment for information sharing and for development of a shared risk-assessment framework to enhance patient safety by mitigating medical device cybersecurity risk
  MITRE is helping FDA shape and implement this vision
Spurred by
  2013 disclosure of medical device vulnerabilities
  EO 13636 and PDD 21
Issued new pre-market and post-market cybersecurity medical device guidance
Convened the stakeholder community in workshops held in Oct 2014 and Jan 2016
  Complete archives are online
Stake Holder Collaboration
Device Industry
Healthcare Organizations
Federal Partners
Researchers & Experts
Enable a platform for maintaining Cybersecurity Awareness – Intentional and unintentional threats
Regulatory Clarity
Premarket expectations
Post market expectations
Post Market Surveillance

## Slide 4: Problem: Different Perspectives of Vulnerabilities and their Severity
Device Manufacturer
  Do I need to patch it now or can I wait for the next upgrade?
Healthcare Provider
  Are there compensating controls or do I have to unplug it from the net?
Patient
  Should I refuse treatment with this device?
FDA
  Do we need to take action?
Vulnerability Researcher
  This is bad and you have to fix it!

## Slide 5: The Delicate Balance of Safety, Security, and Privacy
“Everything is a priority”
Varying risks to patient, device, clinical environment
Different regulatory requirements
Different prioritization depending on context of risk assessment
Each can interfere with the other
  Don’t want anti-virus to fire during surgery
  Security can erode privacy
Our focus: safety and security
Security
Privacy
Safety

## Slide 6: Real-World Vulnerabilities and Scoring Challenges
Can be difficult to determine safety impact of a technical finding
  Safety regulations already require separation and indirect defense-in-depth
  Fail-safe operations
Vulnerable applications might not directly interact with physical actions
  Depends on the functionality and work/data flow
Traditional information technology (IT) often prioritizes integrity and confidentiality over availability
For patient safety, availability is often extremely important
  “You can’t reboot a patient”
The clinical environment varies widely

## Slide 7: Example: Hospira LifeCare PCA Infusion Pump
Technical vulnerability(ies)
  Remote telnet root access without password
  CVSSv2: 10.0 (ICS-CERT)
Healthcare impact
  Change drug libraries, including min/max allowed dosage
  (unproven?) change actual dosage delivered
Defense-in-depth:
  Human still needs to manually confirm dosage change
Environmental considerations
  Pump may be on separate, “trusted” network
  The vulnerable interface might not even be in use
Scoring implications
  In a hospital performing due diligence, risk may be minimal
References
  https://ics-cert.us-cert.gov/advisories/ICSA-15-125-01B
  FDA notice for Symbiq model: http://www.fda.gov/MedicalDevices/Safety/AlertsandNotices/ucm456815.htm
Notes: Image from: https://www.hospira.com/en/products_and_services/infusion_pumps/Lifecare

## Slide 8: BD/CareFusion Pyxis SupplyStation (Drug Cabinet)
Not a regulated medical device, but important to the hospital
Technical vulnerability: use of vulnerable 3rd-party components
Healthcare impact
  Unspecified; “compromise” the cabinet
  Open drug cabinet, steal drugs
Defense-in-depth
  Manual keys can be used to open cabinet
Environmental considerations
  Cabinet typically in physically-secured environment
  May be on isolated networks
Scoring implications
  CVSS v3 might be a 10.0
  No direct risk to patient safety
  … but, delayed delivery of care possible?
References
  https://ics-cert.us-cert.gov/advisories/ICSMA-16-089-01

## Slide 9: High-Level Impacts in a Clinical Setting
Prevent, modify, or delay:
  Therapy
  Diagnosis
  Monitoring and alerting
  Too much, too little, too fast, too slow, too early, too late, or not at all
Reduce efficiency (more manual work)
Pivot to the rest of the network
Privacy loss
Financial loss – billing, reimbursement
Reputation damage
Loss of faith in devices
Notes: Image from:
http://www.carefusion.com/our-products/medication-and-supply-management/medication-and-supply-management-technologies/pyxis-supply-technologies/pyxis-supplystation-system

## Slide 10: Environment Matters
The raw, base CVSS score of a vulnerability has no relationship to the vulnerability’s actual impact on patient safety.

## Slide 11: Desired Features of a Health Care Scoring Method
Minimal complexity
Usable by practitioners
Accepted by diverse stakeholders
  Manufacturers, hospital, security researchers, patients, regulators
Flexible for different clinical environments
Flexible for different device classes
Repeatable (different people come up with same score)
Validated
Provide common “language” for centering discussion and keeping disagreements focused

## Slide 12: Other Risk-Related Metrics and Analysis Frameworks
Hazard analysis
  Pro: focused on safety; well-established; well-known to manufacturers
  Con: unknown to researchers; does not consider sentient, adaptive attacker
CVSS v2
  Pro: widely adopted and validated
  Con: environmental adjustments have minimum effect on score; focused on the “box”
CVSS v3
  Pro: environmental adjustments support more realistic scoring modifications
  Con: not yet widely adopted; more subject to abuse and inconsistency?
CWSS (Common Weakness Scoring System)
  Pro: explicitly accounts for presence of intrinsic and extrinsic controls
  Con: heavy developer focus; less active use; more complex than CVSS
FAIR
  Pro: Heavy adoption by finance industry
  Con: Proprietary

## Slide 13: Common Vulnerability Scoring System (CVSS)
CVSS is an open framework developed by the Forum of Incident Response and Security Teams (FIRST) for communicating the characteristics and severity of software vulnerabilities
  The Base metric group represents the intrinsic qualities of a vulnerability
  The Temporal metric group reflects the characteristics of a vulnerability that change over time
  The Environmental metric group represents the characteristics of a vulnerability that are unique to a user's environment.
Typically only the Base score is computed and often sensationalizes medical device vulnerabilities by ignoring the clinical environment
Access Vector
Access Complexity
Authentication
Confidentiality Impact
Integrity Impact
Availability Impact
Base Metric Group
Exploitability
Remediation Level
Report Confidence
Temporal Metric Group
Collateral Damage Potential
Target Distribution
Confidentiality Requirement
Integrity Requirement
Availability Requirement
Environmental Metric Group

## Slide 14: Adapt CVSS for Healthcare
Healthcare threats
  Collaborate with health care delivery organizations
  Information Sharing and Analysis Organization
  Commercial feeds and reports
Compensating controls
  Manufacturer’s recommendations
  Hospital’s best practices
∆ Exploitability
∆ Impact
∆ Scoring
Adverse events
  Apply natural language processing to extract symptoms of flaws with potential safety impact
Access Vector
Access Complexity
Authentication
Confidentiality Impact
Integrity Impact
Availability Impact
Base Metric Group
Exploitability
Remediation Level
Report Confidence
Temporal
Metric Group
Collateral Damage Potential
Target Distribution
Confidentiality Requirement
Integrity Requirement
Availability Requirement
Environmental Metric Group

## Slide 15: CVSS v 3.0
Exploit Code Maturity
Remediation Level
Report Confidence
Attack Vector Scope
Attack Complexity Confidentiality
Privileges Required Integrity
User Interaction Availability
Confidentiality Requirement
Integrity Requirement
Availability Requirement
Modified Base Score Components
Base Score
Temporal Score
Environmental Score

## Slide 16: CWSS and CWRAF
Technical Impact
Acquired Privilege
Acquired Privilege Layer
Internal Control Effectiveness
Finding Confidence
Base Finding Metric Group
Required Privilege
Required Privilege Layer
Access Vector
Business Impact
Likelihood of Discovery
Likelihood of Exploit
External Control Effectiveness
Prevalence
Environmental Metric Group
Attack Surface Metric Group
Authentication Strength
Level of Interaction
Deployment Scope
The Common Weakness Scoring System (CWSS) provides a mechanism for prioritizing software weaknesses in a consistent, flexible, open manner
Chemical
Energy
E-voting
Web Apps
Control Systems
Embedded Devices
SCADA HMI
Smart Grid House Meter
Domains
Technology Groups
Financial loss, privacy violation
10: Code exec
6: Read memory
3: Crash
Business Value Context
Technical Impact Score
Vignettes
The Common Weakness Risk Assessment Framework (CWRAF) enables CWSS to capture business importance through vignettes

## Slide 17: CWRAF - Business Value Context (BVC)
Identifies critical assets and security concerns
Links Technical Impacts with business implications
More fine-grained model than the CIA Triad
Modify data
Read data
DoS: Unreliable execution
DoS: Resource consumption
5. Execute unauthorized code or commands
6. Gain privileges / assume identity
7. Bypass protection mechanism
8. Hide activities
CWE Technical Impacts

## Slide 18: Simplified Technical Impact Scorecard - Web-based Shopping Cart Vignette
Technical Impact | Weight | Explanation
Modify data | 8 | Modify or delete customer order status and pricing, contact information, inventory tracking, customer credit card numbers, cryptographic keys and passwords (plaintext and encrypted).
Read data | 5 | Read customer credit card numbers, customer credit card numbers, order status, cryptographic keys and passwords (plaintext and unencrypted).
DoS: unreliable execution | 4 | Customers cannot reach site or experience delays in reaching site; delays in order placement and resulting financial loss.
DoS: resource consumption | 4 | Customers cannot reach site or experience delays in reaching site; delays in order placement and resulting financial loss.
Execute code or commands | 10 | … everything 
Gain privileges / assume identity | 6 | Customers can see or modify other customers’ orders
Bypass protection mechanism | 6 | 
Hide activities | 2 | 

## Slide 19: Notional Technical Impact Scorecard – Simplified (BVC: physical safety, ignoring privacy-related regulations)
Technical Impact | Weight | Explanation
Modify data | 8 | 
Read data | 0 | 
DoS: unreliable execution | 2 | 
DoS: resource consumption | 2 | 
Execute code or commands | 10 | 
Gain privileges / assume identity | 6 | 
Bypass protection mechanism | 6 | 
Hide activities | 2 | 

## Slide 20: Scoring Weaknesses Discovered in Code using CWSS

## Slide 21: Leverage CWSS & CWRAF to Generate CVSS Environmental Score
CVE Assigned
Vignettes
(HDO X Device Type)
Environmental
Score
Business Value Context
Technical Impact Scorecard
Vulnerability Discovered
Environmental Score
Confidentiality Requirement
Integrity Requirement
Availability Requirement
Modified Attack Vector
Modified Attack Complexity
Modified Privileges Required
Modified User Interaction
Modified Scope
Modified Confidentiality
Modified Integrity
Modified Availability
Generate “CWSS” Vector

## Slide 22: Medical Device Cybersecurity Risk Management (from DRAFT Postmarket Guidance)
Assessing Exploitability of the Cybersecurity Vulnerability
Assessing Severity Impact to Health
Evaluation of Risk to Essential Clinical Performance

## Slide 23: Map to Essential Clinical Performance
Modify data
Read data
DoS: unreliable execution
DoS: resource consumption
Execute unauthorized code or commands
Gain privileges / assume identity
Bypass protection mechanism
Hide activities
Negligible
Minor
Serious
Critical
Catastrophic
Technical Impacts
Hazards Analysis
(e.g., STPA)
Control Action
Not providing causes hazard
Providing causes hazard
Incorrect timing/order
Stopped too soon/Applied too long
Severity Impact to Health (FDA Post-Market Guidance)
Attack vector
Attack complexity
User interaction
Deployment scope
Maturity of exploit code
CVSS and CWSS elements
Internal control effectiveness
Authentication strength
External control effectiveness
CWSS elements
Low
Medium
High
Controlled
Uncontrolled
Exploitability
Risk to ECP Controlled?

## Slide 24: Some of the challenges/questions
What’s the right level of abstraction for device classes?
  Important for scalability
What’s the right level of abstraction for vulnerabilities?
  Also important for scalability
  CWE taxonomy? NIST’s vulnerability taxonomy?
How do we handle multiple business value contexts, e.g., HIPAA compliance and patient safety?
  Multiple vignettes?
Is computing CVSS environmental score sufficient, or will we need to add elements to the CVSS vector to better reflect the healthcare environment?

## Slide 25: Another Challenge: The “Bill of Materials” and Scoring of 3rd-Party Components
Health care providers want manufacturers to provide a bill of materials for their devices
  “Am I vulnerable to [popular, scary vulnerability]?”
  As of May 2016, only Royal Philips has publicly stated they will do this
3rd-party libraries are often scored in isolation
  Worst-case assessment
3rd-party applications might not have same attack surface
  e.g. use of browser without ability to make remote connections
If “only” a DoS but prevents device operation – bad
If root/admin privileges but only to asset-management component, with strong separation from device functionality – no biggie
  If affected API function is unreachable – no vulnerability (or very low risk)

## Slide 26: Healthcare CVSS Working Group – as of May 17, 2016
Approximately a dozen members
Kickoff telecon held on May 11, 2016
“Whole of Community” Approach with diverse stakeholders
  Manufacturers
  Health care providers
  Security researchers / consultants
  Academia
  Government agencies

## Slide 27: Work Plan
Initial steps
  Identified and invited small team for initial development
    Manufacturers, HDOs, cybersecurity researchers, NIST, ICS-CERT
  Held kick-off telecon May 11
Next steps
  Draft initial vignette for infusion pump 4-6 weeks after kick-off
  Get feedback from broader community
  Iterate…
Later steps
  Additional device areas
  Consider validation of algorithm as Medical Device Development Tool (MDDT)

## Slide 28
Questions?
pc@mitre.org (Penny)
coley@mitre.org (Steve)

## Slide 29
BACKUP / DETAIL SLIDES

## Slide 30: Abbreviations
CIA – Confidentiality, Integrity, Availability
CVE – Common Vulnerabilities and Exposures
CVSS – Common Vulnerability Scoring System
CWE – Common Weakness Enumeration
CWSS – Common Weakness Scoring System
CWRAF – Common Weakness Risk Assessment Framework
ECP – Essential Clinical Performance
ICS-CERT – Industrial Control Systems Computer Emergenct Response Team
STPA – Systems-Theoretic Process Analysis

## Slide 31: Calculating CWSS Impact Weights

## Slide 32: … and qualify it as a Medical Device Development Tool (MDDT)
Three tool types
  Clinical outcome assessment
  Biomarker test
  Nonclinical assessment model
Qualification package
  Description of the tool
  Context of use
  Strength of evidence
  Assessment of advantage and disadvantages of qualifying the tool
MDDTs are scientifically validated tools that can “facilitate the scientific evaluation and assessment of a medical device by providing a more efficient and predictable means for collecting the necessary information to make regulatory assessments.”
MDDTs are scientifically validated tools that can “facilitate the scientific evaluation and assessment of a medical device by providing a more efficient and predictable means for collecting the necessary information to make regulatory assessments.”

## Slide 33: Relation to FDA Work
Developing the context of use
  General framework with specialized vignettes
    Initial focus on infusion pumps
  Use in post-market setting when vulnerabilities are discovered by manufacturers or third parties
  FDA and public health impact
    Manufacturers and third parties have a shared framework for assessing severity of vulnerabilities
    FDA and manufacturers triage vulnerabilities based on ECP
    Reduce sensationalism and reassure public of device safety
Reaching out to community to develop vignettes
  Small initial group drawn from device manufacturers, healthcare delivery organizations, cybersecurity researchers, ICS-CERT, FDA
  Larger group for feedback
Collaboration with MDISS/NH-ISAC MDVISI effort
  Evolving MDRAP to crowd source information about devices
    This work can both inform the data collection and use the data to aid in analysis of technical impacts and compensating controls

## Slide 34: AHRQ Patient Harm Scale
Version 1.1
  Death
  Severe Permanent harm
  Permanent harm
  Temporary harm
  Additional treatment
  Emotional distress or inconvenience
  No harm
Version 1.2 – Temporal elements moved to a separate dimension
  Death
  Severe harm
  Moderate harm
  Mild harm
  No harm
https://pso.ahrq.gov/